## Slide 1: LINT error explanation for design_assignment
16-06-2025
Sharanya Shetty

## Slide 2: LINT errors STARCO5-1.1.5.1
Error: Register output signal name 'rst_sync_2' does not follow recommended naming convention.
Justification: This is purely a naming/style issue, not a functional problem

## Slide 3: LINT errors STARCO5-1.1.5.2b
Error: Register output signal name 'rst_sync_2' does not follow recommended naming convention.
Justification: This is purely a naming/style issue, not a functional problem

## Slide 4: LINT errors STARCO5-1.2.1.1b
Error: Design uses multiple clocks ('adc_clk' and 'ana_clk').
Justification: Multiple clocks are required by system architecture

## Slide 5: LINT errors STARCO5-1.3.2.1a
Error: Gated reset 'sync_inst.gen_synth_net' used for flip-flop 'sync_inst.start_slot_latch' .
Note: same for mid_slot and analog_done
Justification: Asynchronous ack required: synchronizing would miss short pulses, toggle approach would miss rapid consecutive pulses due to feedback delay

## Slide 6: LINT errors STARCO5-1.3.2.1b
Error: Reset 'sync_inst.rst_sync_2' is not generated in a separate module instantiated at top-level.
Justification: Reset synchronization is logically co-located with other CDC functions in the synchronizer module for design simplicity and reduced hierarchy complexity - this is a valid

## Slide 7: LINT errors STARCO5-1.3.2.2
Error: Flip-flop output 'sync_inst.rst_sync_2' used as asynchronous reset for flip-flop 'sync_inst.start_slot_sync_2'.
Justification: This is the correct and intended behavior of a reset synchronizer - rst_sync_2 generates the synchronized reset signal that provides immediate assertion and synchronous deassertion for all downstream flip-flops, which is standard reset distribution methodology.

## Slide 8: LINT errors STARCO5-1.3.2.2
Error: Flip-flop output 'sync_inst.rst_sync_2' used as asynchronous reset for flip-flop 'sync_inst.start_slot_sync_2'.
Justification: This is the correct and intended behavior of a reset synchronizer - rst_sync_2 generates the synchronized reset signal that provides immediate assertion and synchronous deassertion for all downstream flip-flops, which is standard reset distribution methodology.

## Slide 9: LINT errors STARCO5-1.6.2.1
Error: Output port 'analog_start' is not driven by a flip-flop.
Justification: analog_start requires immediate combinational response to start_slot/mid_slot events for precise analog timing control - registering this signal would introduce unacceptable delay in the analog trigger path and violate timing requirements

## Slide 10: LINT errors STARCO5- 2.3.5.1
Error: Flip-flop 'sync_inst.rst_sync_1' has fixed input value '1'.
Justification: This is the correct and intended behavior for a reset synchronizer - the first flip-flop must always load '1' when not in reset to provide proper synchronous reset release timing, which is standard reset synchronizer methodology

## Slide 11: LINT errors STARCO5- 3.1.3.2a
Error: Port 'burst_read' not defined in recommended order.
Justification: This is a port organization style preference - burst_read input is grouped with its related interface signals (trigger_burst_read, read_data, fifo_empty) for logical readability rather than strict input/output ordering, which is a valid design practice for interface grouping

## Slide 12: LINT errors STARCO5- 3.3.1.4a
Error: Asynchronous set/reset 'reset' (flop: 'sync_inst.start_slot_sync_2') not controllable from external pins.
Justification: The reset is controllable through the reset synchronizer chain - rst_n_asyn (external pin) → rst_sync_2 → downstream flip-flops, which provides proper reset distribution with synchronized deassertion while maintaining external controllability through the reset tree.

## Slide 13: LINT errors STARCO5- 3.3.1.4b
Error: Flip-flop 'read_data[19:0]' has neither asynchronous set nor asynchronous reset.
Justification: read_data only needs to be valid during active burst_read operations - the reset state is don't-care since the data is only consumed when explicitly reading from FIFO, making reset unnecessary and saving logic resources.

## Slide 14: LINT errors PortIOConnectionSanity-ML
Error: Input port 'mid_slot_asyn' should be connected to single Input pad cell pin. But connections are: 'sync_inst.I_MUX_...cell:I_MUX_N_39)'.
Justification: the logical connectivity and timing behavior remain correct regardless of the physical pad-to-logic routing implementation.

## Slide 15: LINT errors GateResetAtTop
Error: Gated reset 'sync_inst.rst_sync_2' not generated in a separate module at top-level.
Justification: The synchronized reset is appropriately co-located with other CDC logic in the synchronizer module for design cohesion and simplified hierarchy - this is a valid reset distribution methodology that doesn't require separate top-level reset generation modules.

## Slide 16: LINT errors ExternalPortBranchCheck
Error: Multiple branches existing on net 'mid_slot_asyn' connecting input port 'mid_slot_asyn', 'sync_inst.mid...ms_temp.EN(MUX)'.
Justification: Normal signal fanout behavior - mid_slot_asyn legitimately drives multiple synchronizer logic blocks (pulse latch, data capture enables) which is expected and correct for input signal distribution within the synchronizer module.

## Slide 17: LINT errors ClockName-ML
Error: Clock signal name 'time_clk' does not match the given regular expression pattern.
Justification: This is a descriptive and meaningful clock name that clearly indicates its function for timing control - the naming convention violation is purely stylistic and doesn't affect functionality, logic correctness, or synthesis results.

## Slide 18: LINT errors ClockDomain
Error: Multiple clock domains. First: 'ana_clk'(flop: sync_inst.analog_data_temp[0]), Current: 'clk'(flop: sync_inst.adc_data[0]).
Justification: Multiple clock domains are architecturally required for this mixed-signal interface design - different subsystems (analog, ADC, digital) operate at different frequencies with proper CDC synchronization implemented between all domain crossings.

## Slide 19: LINT errors AvoidAsync
Error: Asynchronous Reset signal 'rst_n_asyn' used at flop 'rst_sync_2'
Justification This is standard reset synchronizer topology - both flip-flops require asynchronous reset connectivity to ensure immediate reset assertion while maintaining synchronous deassertion through the two-stage release sequence.