## Slide 1: 06/06/2025 RTL design assignment
This presentation contains explanation of cases which counts as VALID and INVALID
The presentation contains
  The flow of signal
  Explanation on extra delay
  Design constraints
  Animation to visuial the signal

## Slide 2: 06/06/2025 Understand the flow
Start_slot  Analog_start  Analog delay  Analog_done (Analog_reset)  (Sync Reg)  ADC_trigger  ADC delay  EOC (stable for 5 CC)

## Slide 3: 06/06/2025 Minimum delay from controller perspective
Constraint no.1 : Analog delay > 0
Start slot/Analog start to done register: depends on analog data
start_analog to done register (α) = (analog_delay // N) + 1
ADC trigger to EOC : 1 Tcntrl CC let call it β = constant
Analog delay in analog CC | Delay for Done register in Tcnrl CC
1-3 (Analog freq = f1) | 1 (controller freq = f1/N) (N =4 )
4-7 | 2

## Slide 4: 06/06/2025 Understand the flow
Delay = α + β

## Slide 5: 06/06/2025 Understand the flow
PD<= α + β + 5 : no additional delay
PD> α + β + 5 , then add an additional delay between α , β

## Slide 6: 06/06/2025 Design Constraint
Programmable delay >= start_analog to done register + ADC trigger to EOC
  PD >= α + β
Delay between slots (∆) >= start_analog to done register (α)
  ∆ >= α
Delay between slots + start_analog to done register for current slot_current + ExtraDelay_current >= start_analog to done register for previous slot + ExtraDelay_previous
  ∆ + α2 + ED2 >= α1 + ED1

## Slide 7: 06/06/2025 RTL design assignment flow
Start_slot
Controller start_slot
Start analog
Counter (∆)
Done Analog
Controller ana done
Counter (α)
Counter (α)
Controller ana reset
PD >= α + β
Mid_slot
ControllerMid_slot
Counter (∆)
∆ >= α
Mid_slot
ControllerMid_slot
Counter (∆)

## Slide 8: 06/06/2025 RTL design assignment flow with extra delay
start
C
start
Ana start1
Ana done1
Ana reset1
ADC trigr1
EOC (5cycle) 1
α1
β
ED1
5
mid
C
mid
Extra delay1
Ana start2
Ana done2
Extra delay2
ADC trigr 2
EOC (5cycle) 2
α2
ED2
β
  ∆ + α2 + ED2 >= α1 + ED1
∆
Extra delay2
ADC trigr 2
EOC (5cycle) 2
ED2
β
  ∆ + α2 + ED2 >= α1 + ED1
  PD1
  PD2

## Slide 9: 16/06/2025 Fixed Design Constraint
Due to the way start_slot and mid_slot events are synchronized and tracked, a new mid_slot cannot be initiated until the previous mid_slot process has completed, and the same applies to start_slot. This enforces strict sequencing and prevents overlapping analog capture operations. If this rule is violated design will fail.