## Slide 1: Controller Design Waveform
For more information on the testbench : Testbench_explanation.docx For more information on testplan : Test_Plan.xlsx

## Slide 2: Basic delay test: Normal function with fixed delays
In Figure 1, you can observe that the ADC data from both time slots is correctly combined and stored sequentially in the FIFO.
Figure 1

## Slide 3: FIFO burst read : Continuous ADC read – check if data is stored properly
In Figure 2, a total of 128 ADC data entries are written into the FIFO. These entries are verified using checkers Figure 3, which confirm that the stored data matches the expected values.
Figure 2
Figure 3
Fail1 = 0 indicates no errors

## Slide 4: Delay sweep : Try all delay values from 19 to 31
In Figure 4, the programmable delay values for both the start slot and mid slot range from 19 to 31. The signal fail_2 = 0 confirms that the data has been correctly written to and read from the FIFO without any mismatches.
Figure 4

## Slide 5: Delta sweep : Try all delay values from 36 to 255
Figure 5
Figure 6

## Slide 6: Delta sweep : Try all delay values from 36 to 255
In Figure 5, the delay values are varied from 36 to 255 for both the start-to-mid and mid-to-start intervals, covering a wide range of timing conditions.
Figure 6 provides a zoomed-in view of the signal transitions to closely observe the slot behavior and ADC activity.
In each test case, 128 values are successfully written to and verified from the FIFO. The signal fail6 = 0 confirms that no errors occurred during the process.

## Slide 7: Fifo Overflow and Overwrite before Read​
In Figure 7, the low storage warning is triggered once the FIFO count reaches 100, and it remains asserted thereafter. Since the previously written data is not read, the FIFO becomes full and cannot accept new data. As a result, even though the wr_en signal is active, no further data is written, preventing any overwriting.
Figure 7

## Slide 8: Read and Write : Check if the system can read and write together
In Figure 8, it is evident that the system is capable of simultaneous read and write operations, demonstrating the asynchronous nature of the FIFO design.
Figure 8

## Slide 9: Reset check :Give reset in between and see recovery
In Figure 9, the FIFO is initially full, and upon asserting reset, the FIFO is cleared and becomes empty. This confirms that the reset mechanism functions correctly, effectively clearing the stored data.
Figure 9

## Slide 10: Long analog delay: If analog_delay > max_ana_delay, data should be missed or flagged
In Figure 10, three test cases are illustrated:
Case 1: Both the start slot and mid slot have analog delays exceeding the maximum allowed. As a result, a timeout is triggered, and no data is saved. Fail3 = 0
Figure 10

## Slide 11: Long analog delay: If analog_delay > max_ana_delay, data should be missed or flagged
In Figure 10, three test cases are illustrated:
Case 2: Only the start slot has a delay greater than theallowed limit. Again, no data is stored due to the timeoutcondition. (fail4 = 0)
Case 3: The mid slot has an excessive analog delay, andconsequently, no data is saved for that slot. (fail5 = 0)
This confirms that the system correctly handles timeoutconditions and avoids storing invalid data.

## Slide 12: Different clock speeds : Run tests with different clk periods
Figure 11

## Slide 13: Different clock speeds : Run tests with different clk periods
In Figure 11, tests were performed under various clock period configurations. The fail flags are all 0, confirming that all 9 test cases passed under each setting, demonstrating the design’s robustness across different clock domains. Additionally, in the console output, both the expected (values and actual values are printed, enabling manual verification and debugging if required.